New Mini Frequency Inverter Delivers High Performance in a Tiny Package

WEG’s new CFW100 is one of the world’s most compact frequency inverters.

WEG, a leading supplier of drive technology, power generation and distribution as well as automation solutions, has added the CFW100 mini frequency inverter to its line of frequency inverters. This compact inverter is available in three sizes (A, B and C) for rated motor power from 0,18 to 0,75 kW and rated current from 1.6 to 4.2 A. With a height of 100 to 126 mm, a width of 55 mm and a depth of 129 mm, the CFW100 units are among the smallest frequency inverters currently available offering many applications at the user’s fingertips. The mini frequency inverters with integrated micro-PLC are particularly suited to simple technical applications in the commercial and consumer sector, such as swimming pool pumps, motorised hospital beds, lift doors and fitness equipment, as well as small fans or mixing machines and special-purpose machines. With its combination of extensive functionality and extremely small size, the CFW100 is easy to integrate into electrical cabinets and machines. This gives users an especially compact and cost-effective solution for controlling the speed of three-phase induction motors.

Along with the integrated micro-PLC, which supports IEC 61131-3 compatible programming, the CFW100 features an intuitive human-machine interface (HMI) with an LCD display. The plug-and-play design of the new frequency inverter makes installation and commissioning especially easy. As part of the modular CFW100 platform architecture, WEG offers various plug-in base terminals, including USB and Modbus RTU communication interfaces, to facilitate easy access to major field bus systems such as Modbus, DeviceNet or CANopen. Extension modules are also available to enable remote control of the device with an HMI/keypad or an infrared remote control. An optional flash memory card with integrated copy and paste functions allows parameter data sets to be saved and transferred conveniently. A Bluetooth link can also be implemented with an accessory plug-in module. The low-maintenance device concept additionally includes an easily replaceable ventilation module for size B and C units.

The CFW100 operates three-phase motors from single-phase 200 to 240 V supply (50/60 Hz). It has an overload capacity of 150% of rated current for an interval of 60 seconds every 10 minutes. Voltage vector control (VVC) and V/f characteristic curve control are supported for driving three-phase induction motors. The CFW100 has electronic thermal protection capability to prevent motor overheating and four digital inputs as standard, with possibility to increase by expansion plug-in module. The enclosure protection rating is IP20, and the mini frequency inverter can be used at ambient temperatures up to 50°C without derating. Another bonus feature is the SuperDrive G2 setup software for free downloading on WEG website.

Figure caption:

WEG1752_figure 1: WEG’s new CF100 mini frequency inverter – many applications at your fingertips

## About WEG

A global major in the power distribution, automation and control sectors, WEG has just celebrated its 50th birthday. The company’s global sales now exceed the US$3-billion mark, representing increasing global success across a wide range of product groups, including the latest generation of transformers, LV control gear, generators,  gear motors, inverter drive systems, soft starters, LV and HV motors, ATEX- compliant explosion proof motors, smoke extraction motors and full turnkey systems. In addition, WEG has recently made a significant strategic expansion of its product portfolio, following the establishment of a joint venture for the manufacturing of wind turbines and the purchase of an Austrian gearbox manufacturer, WATT Drive.

Editor Contact

Emma Letessier, Technical Publicity
Tel: +44 (0)1582 390980 Mob: +44 (0)7837127613
Email: eletessier@technical-group.com

Company Contact

Marek Lukaszczyk, WEG Electric Motors (UK) Ltd 
Tel: +44(0)1527 513800 Fax: +44(0)1527 513810

Web: www.weg.net 
Email:  wegsales@wegelectricmotors.co.uk

Web: www.weg.net, www.wattdrive.com   Informationen zu WEG

WEG ist ein weltweit operierender, führender Anbieter für Lösungen in der Antriebstechnik, Energieerzeugung und -verteilung sowie in der Automatisierungstechnik und im Schaltanlagenbau. 1961 in Brasilien von drei Unternehmern mit deutschen Vorfahren gegründet, hat sich WEG zu einem der wichtigsten Hersteller für Elektromotoren weltweit entwickelt. Mit Produktionsstandorten in Brasilien, Argentinien, Mexiko, USA, Österreich, Portugal, China, Indien und Südafrika sowie weiteren Niederlassungen auf der ganzen Welt konnte das Unternehmen im Kalenderjahr 2012 einen Jahresumsatz von 2,4 Milliarden Euro und zweistellige Wachstumsraten erwirtschaften.

Dank des breiten Portfolios und der hohen Fertigungstiefe kann der Hersteller in der elektrischen Antriebstechnik innovative Komplettlösungen anbieten. Dazu zählen eine Reihe von Produktgruppen, darunter Niederspannungs- und Hochspannungsmotoren, Transformatoren, Generatoren, Getriebemotoren, Schalt- und Regelgeräte, Frequenzumrichter, Softstarter, ATEX-konforme, explosionsgeschützte Motoren, Brandgasmotoren sowie schlüsselfertige Komplettsysteme. Mit den Induktionsmotoren der W22-Baureihe bietet WEG zudem eine der branchenweit breitesten Paletten an energieeffizienten Motoren an (IE1-IE4) und nimmt damit in der Branche eine Vorreiterrolle ein.

Weltweit beschäftigt WEG etwa 24.000 Mitarbeiter, davon etwa 120 in Deutschland. Durch die Übernahme der österreichischen Watt Drive Antriebstechnik GmbH Ende 2011 hat die Unternehmensgruppe sowohl ihr Produktportfolio auf Getriebe und Getriebemotoren erweitert als auch ihre Präsenz im deutschsprachigen Raum ausgebaut.

Redaktioneller Kontakt / Belegexemplare bitte an:

Mark Herten, Technical Publicity

Postfach 12 55, 21232 Buchholz
Tel: +49 (0)4181 968 0982 Mob: +49 (0)1520 748 3901
E-Mail: mherten@technical-group.com

Kontakt zum Unternehmen in Deutschland:

WEG GERMANY GmbH

Industriegebiet Türnich 3, Geigerstraße 7, D-50169 Kerpen-Türnich

Tel: +49 (0)2237/9291-0 Fax: +49 (0)2237/9291-200

Jürgen Ponweiser, E-Mail: ponweiser@wattdrive.com

Kontakt zum Unternehmen in Österreich:

Watt Drive Antriebstechnik GmbH

Wöllersdorfer Str. 68, A-2753 Markt Piesting

Tel: +43 (0)2633 404-0, Fax: +43 (0)2633 404-220

Jürgen Ponweiser, E-Mail: ponweiser@wattdrive.com

Web: www.weg.net, www.wattdrive.com